## Slide 1
FTIR · EC CALIBRATION · ADDIS ABABA · ANN 1:1 · 12 AUG 2026
What changed —
and what needs your call.
Three committed results on the intercept · one open question resolved this morning · six decisions before tomorrow's 10:00 with Satoshi.
Every number traces to a committed, executed notebook (ftir_11–27) except where a slide says otherwise. Focus: FTIR, HIPS, TOR and the IMPROVE network.
Notes: Three things landed since you last saw this, and I need six decisions before tomorrow morning. The deck for Satoshi is built and it has not gone anywhere. Nothing here has been said out loud outside this room.

## Slide 2
STATUS AT A GLANCE
Since you saw it — and what needs you today.
Since you saw it
Audit: the random-cohort claim corrected in deck, summary and email
pushed
Intercept restated as a MAC-invariant ~21 Mm⁻¹ absorption target (ftir_25)
committed
“The offset lives in x” survives its sharpest cheap test (AIRSpec gain)
committed
IMPROVE HIPS reads ≈ 0 at EC = 0 — not a generic HIPS zero (ftir_26)
committed
Both ChemSpec carbon columns circular — no independent EC reference in hand (ftir_27)
committed
HIPS wavelength resolved: He–Ne 632.8 ≈ 633 nm, MAC 10 at 633
resolved today
ftir_24 (dry vs non-dry) is buildable today — the 43-undated worry is retired
ready
Needs you today
Approve the Satoshi deck — five parts, six asks, two tone calls
sign off
What does SPARTAN mean by HIPS_Uncertainty / HIPS_MDL?
semantics
ftir_24 — build today, or after tomorrow?
go / no-go
Who owns each of tomorrow's asks in the room?
assign
Quartz-TOR one-pager — hand to Satoshi tomorrow?
go / no-go
Hossein outcome — it gates the co-author email
blocked on you
Notes: Let her read the scorecard while you give the opening line. Do not walk it row by row. Everything green is committed and pushed; the gold column is the decision list for this meeting.

## Slide 3
01 · THE AUDIT — CAUGHT BEFORE SATOSHI, NOT AFTER
The random-cohort claim was wrong on all three counts — and never comparable anyway.
5
“ten” cohorts
3.10–5.00
“4.4–7.3” range
beats OCEC-800
random #3
Each cohort was scored on its own disjoint-site split (n_test 114–194) — those RMSEs were never comparable across rows. The claim is out of the deck, the summary and the email draft.
The conclusion survives on like-for-like evidence: same 190 Addis filters — RMSE 1.16 vs 1.48–2.24; held-out TOR R² 0.911 vs 0.594–0.775.
Also corrected: VIP ρ = 0.74/0.12 flagged uncorroborated (no executed notebook computes it); −1.61 → −1.62; ETBI contrast now vs Addis Dry median 43.2; “~91% baseline” qualified as one representative filter.
fix pushed 53c332e
like-for-like RMSE 1.16 vs 1.48–2.24
held-out TOR R² 0.911 vs 0.594–0.775
Notes: Frame it as the check working, not as damage. The number came in through the summary and propagated outward; no executed notebook ever produced it — that is the signature to watch for. If she asks what else changed: VIP flagged uncorroborated and pulled, the −1.61/−1.62 fix, ETBI vs Dry median 43.2, and the 91% line qualified as one filter.

## Slide 4
02 · WHERE THIS STARTED
The deployed calibration reads y = 1.90x − 4.17 at Addis.
ftir_17 · deployed_alldata_crossplot Fixed 190-filter cohort; deployed predictions exist only for these
Nothing at Addis has negative EC — the offset is the model, not the air.
At MAC 6 the slope pivots to 1.14 but the intercept stays at −4.17: the intercept column is MAC-proof (proved on slide 12).
MAC 10 1.90x − 4.17
MAC 6 1.14x − 4.17
Notes: Thirty seconds — she knows this plot. It is here so the new results have their reference point on screen.

## Slide 5
03 · ANN'S COHORT
Addis-like composition is the extreme tail of IMPROVE — 800 of 13,010 filters.
deck · filtering_by_ocec Cutoff OC/EC ≤ 2.27; pool median 5.54; Addis ≈ 1, below the whole range
Your low-OC/EC idea remains the best locked calibration — and cohort engineering beyond it breaks the held-out TOR test, so OCEC-800 (+ AIRSpec) is the terminal IMPROVE-only candidate.
cutoff OC/EC ≤ 2.27
held-out TOR RMSE 3.4 µg/filter
Notes: Also quick — context for the setup matrix. The random-cohort caveat from slide 01 does not change this ranking; the like-for-like tests do the work now.

## Slide 6
04 · EVERY TRAINING CHOICE, ONE TABLE
Lowest-OC/EC + AIRSpec ends at −1.62 — and is protocol-robust.
by_protocol/site_held_out · calibration_setup_matrix Row 1 is the whole IMPROVE network — ETAD spectra are evaluation-only
The intercept ladder: −4.17 → −3.22 → −1.62.
The corrected setup barely moves between protocols (−1.65 / −1.62) and passes the disjoint-site TOR test (slope 1.01, R² 0.90).
intercept −1.62
protocol-robust −1.65 / −1.62
Notes: One tone call for tomorrow lives on this slide: MAC 10 is where the corrected model “lands closest” — deliberately not “self-consistent”, because 0.86 fails ftir_19's own |slope−1| ≤ 0.1 bar while the raw models at MAC 6 pass it.

## Slide 7
05 · WHY BASELINING MOVES THE ANSWER
~91% of a raw Addis spectrum at the CH band is background — and Addis rides a higher background than its cohort.
deck · airspec_1_baseline One real filter (median-like); grey = all 239 Addis spectra
deck · airspec_3_background_gap Baseline at 2920 cm⁻¹ per filter: cohort 0.101 vs Addis 0.170
baseline share @ CH ~91% (one filter)
Addis vs cohort baseline 0.170 vs 0.101
intercept −3.22 → −1.62
Notes: She has seen these; keep it to the mechanism sentence: a raw-spectra model is free to regress on background, Addis rides a higher background than anything it was trained on, and that error lands as an offset. Honest cost: corrected R² 0.66 vs 0.77 raw and RMSE 2.41 vs 1.16 — we prefer it for its residual structure, not its fit.

## Slide 8
06 · RESURFACED — JULY SLIDE 15, NEVER PRESENTED
The AIRSpec improvement is real — and so is what remains.
ftir_15 · bootstrap_intercepts Site-cluster bootstrap, B = 200; deployed −4.17 dotted
Skipped in July's jump from the cohort sweep to seasonality.
The raw and corrected distributions are fully disjoint — the improvement is not a lucky draw — and the corrected interval still excludes zero: the remaining offset is not noise.
Corrected 95% CI [−1.78, −1.06]; raw [−4.88, −2.81].
corrected CI excludes 0
distributions disjoint
Notes: This is the uncertainty evidence the July meeting never saw. It is the statistical backbone under the intercept work — and the natural bridge into restating that remainder as a physical target, which is the next slide.

## Slide 9
07 · RESURFACED — JULY SLIDE 16, NEVER PRESENTED
The corrected model misses by a flat constant — and Dry was already separating.
ftir_15 · residual_vs_D2_by_season Residual vs Mahalanobis D² in score space, colored by Naveed's seasons
Raw model: error tracks extrapolation distance (r = 0.71) and flips sign by season.
Corrected model: D²-independent, a season-stable −2.0 to −2.6 µg/m³ — and in both panels the Dry points sit lowest.
The season structure slide 15 quantifies was visible here first.
raw: resid ~ D² r = 0.71
corrected offset −2.0…−2.6
Dry lowest in both
Notes: Ironically this is the slide that most directly answered her “I'm confused” moment in July. A constant offset that does not grow with extrapolation distance is not a domain failure — it behaves like something additive sitting in the x-axis data.

## Slide 10
08 · RESULT — THE INTERCEPT, RESTATED (FTIR_25, COMMITTED)
~21 Mm⁻¹ of absorption with no FTIR-EC behind it — and no modelling choice moves it.
Calibration setup | intercept | slope @10 | C (Mm⁻¹)
Whole IMPROVE network (deployed) | −4.17 | 1.90 | 21.9
Biomass-smoke (906) | −6.91 | 2.65 | 26.1
Ethiopia-shaped smoke (300) | −3.69 | 1.75 | 21.1
Spectral analogs (500) | −6.43 | 2.91 | 22.1
Lowest-OC/EC (800) | −3.22 | 1.59 | 20.3
Lowest-OC/EC + AIRSpec | −1.62 | 0.86 | 18.8
21.5
Mm⁻¹ median — 46% of a typical Addis filter's Fabs. Slopes span 3.4× across these six setups; C spans 1.4×. And C is exactly MAC-invariant, so the target survives the MAC fork.
Sharpest cheap test, passed: AIRSpec touches only the spectra (y-side) yet halves slope and intercept in proportion — under y = a(x − c), c stays put: 2.03 → 1.88 (−7.3% where a and b each move ~50%). The offset behaves as if it lives in the Fabs axis.
Stated caveat: C is invariant to any rescaling of the EC axis, so cross-setup stability is partly structural. The claim is “robust to every scaling choice” — not “six independent routes agree”.
Notes: This is the answer to your July question — why is the intercept negative when nothing at Addis is. Set predicted EC to zero and the intercept becomes a quantity you could go and look for: about 21 inverse megametres at the HIPS wavelength with no FTIR-EC behind it. If she pushes on what it licenses: nothing about the cause on its own — the next slide starts eliminating candidates.

## Slide 11
09 · RESULT — IS IT A GENERIC HIPS ZERO? (FTIR_26, COMMITTED)
No. IMPROVE HIPS runs through the origin — which leaves two explanations that are not an absorber.
≤ 1.3 Mm⁻¹
pooled intercept, hard upper bound
+0.12 Mm⁻¹
median Fabs at EC ≤ 0 (n = 4,247)
0.010%
IMPROVE filters reaching Addis's median 47.1
So the offset is Addis-specific: ≤ 6% of C is instrument-generic, and OLS is the maximum over all errors-in-variables fits, so the bound is hard. But two non-absorber explanations survive — hear them today, not tomorrow:
① Curve geometry. Fabs is concave in EC across IMPROVE (≈ EC^0.796, through zero) — a straight line through a concave cloud manufactures a negative intercept with no offset present. Per-site intercepts run at median 35% of site mean Fabs; Addis is 46%, and ~a third of IMPROVE sites sit at or above that in data whose true offset is ~0. (The exponent is an upper bound on concavity — binned on Fabs it comes out faintly convex — so this may be smaller than it looks.)
② A loading-dependent HIPS artifact. IMPROVE median Fabs is 1.3 vs Addis 47 — a 37× gap that rules out an additive loading-independent offset but not one growing with loading: per-site intercept grows with loading (r = 0.69), extrapolating to 16.2 Mm⁻¹ ≈ 75% of C. That extrapolation is 6× beyond IMPROVE's largest site — it cannot be closed from IMPROVE data.
Notes: Give this slide the most air. The generic-zero door is closed with committed numbers. What survives: curvature and a loading-dependent artifact — and real non-EC absorption, which nothing in hand can now separate, because of the next slide. That four-directions narrowing is the case for quartz TOR.

## Slide 12
10 · RESULT — NO INDEPENDENT EC REFERENCE EXISTS IN HAND (FTIR_27, COMMITTED)
Both ChemSpec carbon columns are circular — BC with Fabs, EC with our own FTIR-EC.
ChemSpec_BC = round(Fabs/10, 2)
bit-for-bit on 163/188 ETAD filters; 23 of 25 SPARTAN sites give a BC slope within 1% of 10. Circular with the x-axis.
ChemSpec_EC = EC_ftir, rounded
r² = 0.9997, ratio median 1.0000, median |Δ| = 0.0030 µg/m³ — exactly the 2-dp rounding half-width; exact on 164/175. Circular with the y-axis.
I briefly wrote ChemSpec_EC up as the independent reference; the audit standard caught it within hours — the tell was that its R² against Fabs matches FTIR-EC's own, because it is FTIR-EC. Corrected and pushed.
Consequence: nothing in the committed data can arbitrate between the surviving explanations — or the MAC fork. Every EC reference we hold is circular with one axis or the other. That is what promotes quartz TOR from one ask to the ask.
independent EC references in hand 0
what separates the survivors quartz TOR
Notes: Get ahead of it: if she read ftir_25 yesterday, she saw the wrong version. Say plainly that the correction standard caught your own error the same way it caught the audit items — that is the system working. ChemSpec_OC is circular too. The three proofs: bit-for-bit rounding lattice, the shared per-filter volume-revision ratio across BC/EC/OC, and the network-wide slope of 10.

## Slide 13
11 · RESOLVED THIS MORNING
HIPS is the He–Ne line: 632.8 ≈ 633 nm — and MAC 10 belongs to 633.
633
nm — He–Ne 632.8, rounded. MAC = 10 m²/g at 633.
Sources, both SPARTAN-side: the Instruments page (HeNe laser, 632 nm — and it names your group as running the HIPS analysis) and the 2025 SPARTAN methods paper (He–Ne at 633 nm; MAC 10 at 633). IMPROVE literature reports 633. The 632/633 spread is rounding of the same laser line.
Consequences: the 405 nm premise in RESEARCH_PROGRESS was wrong and is corrected — so the AERONET dust null was aimed at the right wavelength after all, and dust absorbs less at 633 than 405, so that null strengthens and narrows “real non-EC absorption” toward brown carbon. And classic BrC absorbs weakly at 633 — so the non-absorber explanations gain weight correspondingly. The headline ask is untouched: quartz TOR separates the survivors at any wavelength.
Remaining question — semantics, not existence: HIPS_Uncertainty exists as its own parameter row (190/190, median 2.91 Mm⁻¹ = 6.2% of Fabs → Deming λ* ≈ 3, and λ = 1 overstates the EIV intercept correction by ~55%). Is that field counting statistics, repeatability, or propagated calibration uncertainty?
λ 632.8 ≈ 633 nm
MAC 10 @ 633
HIPS_Uncertainty 190/190
λ* ≈ 2.96
Notes: If she asks who confirmed it: Ahmad, this morning, from SPARTAN's public Instruments page and the 2025 methods paper — SPARTAN-side sources, which is exactly what the optics reference said was missing. If she cannot answer the semantics question today, assign the ask: who emails SPARTAN, before or after tomorrow.

## Slide 14
12 · THE MAC FORK, IN TWO FIGURES
MAC cannot move any intercept — and the IMPROVE bridge puts MAC ≈ 10 at Addis-like composition.
ftir_19 · mac_slope_pivot x = Fabs/MAC: intercept and R² exact, slope ×0.6 going 10 → 6
ftir_16 · improve_implied_mac_curve Implied MAC = Fabs / TOR-EC, 151,843 matched filters
Addis-like subset (n = 6,503) MAC 10.05
pool median 11.96
high-OC/EC tail 19.8
Notes: Left: the fork is a slope contest — the intercept column is algebra-proof. Right: quote 10.05 only with its qualifier — the Addis-like OC/EC ≤ 2.27 subset, 6,503 filters; the pool median is 11.96. The inflated high-OC/EC tail independently shows Fabs carries organic-scaling non-EC absorption.

## Slide 15
13 · THE 1600 BAND — WITH JULY'S BURNING SIGNATURE, RESURFACED
Charring grows aromatic C=C at ~1600 — a process argument, not just a correlation.
ftir_12 · peak_center_1600_by_group Addis 1617–1619 cm⁻¹ in every season; IMPROVE ≥ 1633
July-17 deck · slide 23 (McCall) Δ from raw feedstock: O–H and aliphatic C–H destroyed, aromatic C=C grown
Addis center 1617–1619
char peak ~1590–1600
amine rejected (ftir_12)
Notes: The burning-signature panel was never walked through in July. Honesty note for the room: char peaks near 1590–1600, Addis at 1617–1619 — charcoal-consistent, not charcoal-matched. Carboxylate vs aromatic C=C still cannot be separated on Teflon below 1425 — that is the sub-1500 model ask to Satoshi tomorrow.

## Slide 16
14 · THE JUSTIFICATION YOU ASKED FOR — JULY SLIDES 30 & 27, SAID OUT LOUD
A mixture component found with no season labels isolates the anomaly — and it is Oct–Feb.
July-17 deck · slide 30 Low-similarity component fitted season-blind (circled) — almost entirely Dry
July-17 deck · slide 27 Share anomalous by month: Nov 0.82, Dec 0.61 — ≈ 0 May–Sep
Nov 0.82 anomalous
May–Sep ≈ 0
season labels used none
Notes: This replaces the analog R-values you rightly called hand-wavy. A season-blind statistical structure that recovers the seasons on its own is a categorically stronger argument. With the residual panel (slide 07) and the band ratios, three independent views isolate the same Oct–Feb anomaly.

## Slide 17
15 · FTIR_24 — YOUR HYPOTHESIS, TESTED AGAINST COMMITTED NUMBERS
“Dry is right, wet breaks” comes out inverted — and only for the raw model.
ftir_17 · addis_spectra_by_season Dry Oct–Feb / Belg / Kiremt; season moves loading, not shape
Raw-model residuals by season: Dry −1.25 (worst), Belg −0.47, Kiremt +0.49 (best). Corrected: season-stable −2.0…−2.6. Season sensitivity is a raw-model phenomenon.
Design constraint: Dry spans only ~55% of the wet x-range, so naive per-season slopes attenuate mechanically. It must be a pooled fit with a season × x interaction, not three crossplots.
Feasibility: buildable today (~1 GB pull, ~5 min regen); all 43 undated spectra fall outside the 239-filter evaluation set (105 / 61 / 73). Convention: dry_feb headline, belg_feb sensitivity.
Decision: build today, or after tomorrow?
Notes: If she wants it in tomorrow's deck: doable only with the go-ahead now, and say plainly that a result built this afternoon has had no audit pass — the last unaudited number that reached a deck is slide 01's correction. February moves 22 of 239 filters between conventions, so name the calendar on every seasonal number.

## Slide 18
16 · THE ASK THAT SEPARATES THE SURVIVORS
Quartz TOR is now the ask — every EC reference we hold is circular with one axis or the other.
context · adama_etbi_context Adama TOR sits at the IMPROVE median; Bishoftu (ETBI) unused, 26 HIPS filters
Four-direction narrowing: not a generic HIPS zero (ftir_26) · not the FTIR zero (slide 07's flat, D²-independent structure) · no in-hand reference can discriminate (ftir_27) · and the survivors — loading artifact, curve geometry, real absorption — all yield to a co-located quartz-TOR campaign.
Spec (ftir_16, committed): each day separates MAC 6 from MAC 10 by ~3σ → 11–13 days per season, ~36 filters in total (12 + 13 + 11). TOR needs quartz; archived Teflon cannot substitute; Adama Batch-54 proves the chain works.
Pre-registered before any data: if the ~21 Mm⁻¹ were a persistent background, ETBI (median 26.9 Mm⁻¹) would be mostly background — its FTIR-EC should come out very low the day its spectra arrive.
days per season 11–13
filters TOTAL ~36
one-pager committed, ready to hand over
Notes: Say “thirty-six filters total” — never per season; getting it wrong triples the ask. The one-pager is written and committed; the decision is whether it goes to Satoshi tomorrow.

## Slide 19
TODAY'S DECISIONS
Six calls, then tomorrow is mechanical.
① Approve the Satoshi deck
Five parts, six asks — two tone calls: the Calibration-app framing, and how hard to push MAC ≈ 10.
② HIPS_Uncertainty semantics
Counting statistics, repeatability, or propagated calibration uncertainty? If unknown — assign who emails SPARTAN.
③ ftir_24 — today or after?
Buildable this afternoon with the season × x design; unaudited if it goes straight to a deck.
④ Ask owners for tomorrow
Quartz TOR (headline) · Emily Lee's charcoal spectra · sub-1500 model · INDH/CHTS/ETBI pull · ATR go/no-go · baselining trade-off.
⑤ Quartz-TOR one-pager
Committed and ready — does it go to Satoshi tomorrow?
⑥ Hossein outcome
Gates the co-author email; nothing else can unblock it.
Standing rule: nothing reaches Satoshi or the co-authors until you have approved it. That is what today is for.
Notes: Walk the six cards and get a yes/no or an owner on each. The two that cannot slip: the deck approval and Hossein. Then the evening pass folds today's results into the Satoshi deck — mechanical once this content is approved.