## Slide 1
Follow up meeting
FTIR EC at Addis Ababa · 13 Aug 2026 · every figure regenerated in ftir_31
Notes: SAY: Thanks both for making time — Naveed, good to have you back on this thread. The plan: a quick pass through where the Addis EC calibration stands, then the parts where we specifically need your input, Satoshi — baselining, component counts, and what could finally separate the explanations we have left. Every figure today regenerates from one executed notebook, so anything you want to poke at, I can pull the code up live.

## Slide 2
How we choose components — one rule, drawn on the curve it ran on.
Site-grouped 5-fold CV, first major minimum — the same rule for all six setups.
Verified this week: biomass-smoke's k = 4 is the global minimum of this curve (selection_decisions table). The earlier “looks like six” came from a different, overlaid figure.
The app protocol (interleaved 10-fold, within-5%) picks k = 17–27 on the same cohorts.
rule site-grouped · first major min
smoke k = 4 global minimum
app k 17–27
ftir_31 §1.5 · ftir_23 Each cohort's CV curve with ±1 SE ribbon, local minima, and the chosen k marked
Notes: SAY: Since you'll ask how k was chosen: one rule everywhere — site-grouped five-fold CV, first major minimum. This shows each cohort's curve with the rule's machinery drawn on it: the standard-error ribbon and every local minimum, with the chosen k marked. Two things we verified this week after Ann pushed: for biomass-smoke, k equals four IS the global minimum of this curve — the earlier confusion came from a different figure that overlaid full-cohort curves from both fold schemes. And the app protocol's interleaved CV picks seventeen to twenty-seven components on these same cohorts. QUESTION FOR SATOSHI: is four or five components defensible, especially on baseline-corrected spectra? Ann's worry is the first few factors can be mostly Teflon on raw spectra. And when comparing across models, do the component counts need to match — should we run five-for-all and twenty-for-all as a control?

## Slide 3
Same six setups, two component protocols — the swing is the finding.
Left: site-held-out. Right: Calibration app. Same filters, same PLS math.
Smoke-906 swings −0.99 ↔ −6.91 on the component protocol alone; the corrected setup moves −1.62 ↔ −1.65.
Interleaved CV is row-order dependent (k = 15/18/19 on reorderings); site-grouped returns k = 5 every time.
smoke by protocol −0.99 ↔ −6.91
corrected −1.62 ↔ −1.65
ftir_31 §1.6 site-held-out
ftir_31 §1.6 calibration-app
Notes: SAY: This is the comparison Ann asked for — everything twice. Left ladder is our site-held-out protocol, right is the Calibration-app protocol, same filters. Biomass-smoke swings from minus zero-point-nine-nine to minus six-point-nine on the component choice alone — that swing is bigger than anything MAC can do. The corrected setup basically doesn't move: minus one-point-six-two versus minus one-point-six-five. One more committed detail: interleaved CV is row-order dependent — the same 800 filters give k of fifteen, eighteen or nineteen depending on row order; site-grouped gives five every time. Framing discipline: this is not a criticism of the app as a tool — interleaved CV answers a different question than transfer to a site nobody has seen. Addis is exactly that site.

## Slide 4
The problem: the deployed calibration reads y = 1.90x − 4.17 at Addis.
Nothing at Addis has negative EC — the offset is the model, not the air.
At MAC 6 the slope pivots to 1.14 but the intercept stays at −4.17. All intercepts today are µg/m³.
MAC 10 1.90x − 4.17
MAC 6 1.14x − 4.17
ftir_31 §4 Fixed 190-filter cohort; fits asserted against committed values in-notebook
Notes: SAY: The anchor plot. The network calibration carried to Addis is steep with a deep negative intercept — and nothing at Addis has negative EC, so the offset is the model, not the air. Note the right panel: at MAC six the slope pivots to one-point-one-four but the intercept stays at exactly minus four-point-one-seven. We'll prove that invariance in a minute — it kills a whole family of would-be fixes. Intercepts are micrograms per cubic metre everywhere today.

## Slide 5
Addis-like composition is the extreme tail of IMPROVE — 800 of 13,010 filters.
The 800 lowest-OC/EC filters (≤ 2.27 vs pool median 5.54) are the closest IMPROVE gets to Addis. Like-for-like they win: same-190 RMSE 1.16 vs 1.48–2.24; held-out TOR R² 0.911 vs 0.59–0.78.
New: Ethiopia-shaped-300 ∩ lowest-OC/EC-800 = 1 filter. Shape and composition select disjoint filters.
cutoff OC/EC ≤ 2.27
300 ∩ 800 overlap 1 filter
held-out TOR R² 0.911 vs 0.59–0.78
ftir_31 §2.1 n = 12,962 with TOR pairs (48 of 13,010 lack them)
Notes: SAY: Ann's cohort idea: take the 800 lowest-OC/EC filters, the closest IMPROVE gets to Addis composition. Like-for-like it wins — same 190 Addis filters, RMSE one-point-one-six against one-point-five to two-point-two, held-out TOR R-squared point-nine-one against point-six to point-eight. New since yesterday, answering Ann's question: the Ethiopia-shaped-300 and this 800 share exactly ONE filter. Shape-similarity and composition-similarity select disjoint filters — which fits their opposite behaviour, since the shape-selected cohort fails the held-out TOR test. QUESTION FOR SATOSHI: why would spectral-shape similarity fail to track composition here — is that the baseline swamping the shape metric too? IF ASKED about the histogram n: 12,962 is the pool with TOR pairs; 48 of the 13,010 lack them.

## Slide 6
Lowest-OC/EC + baseline correction ends at −1.62 — and is protocol-robust.
The intercept ladder: −4.17 (deployed) → −3.22 (lowest-OC/EC raw) → −1.62 (+ baseline correction).
Passes the disjoint-site TOR test cleanly (slope 1.01, R² 0.90) — and engineering beyond it breaks that test.
corrected intercept −1.62 µg/m³
protocol-robust −1.65 / −1.62
held-out TOR 1.01x · R² 0.90
ftir_31 §1.1 Site-held-out protocol; intercepts µg/m³; row 1 = whole IMPROVE network, ETAD is evaluation-only
Notes: SAY: Every training choice on one table, site-held-out protocol, intercepts in micrograms per cubic metre. The ladder runs minus four-point-two, minus three-point-two, minus one-point-six. Two rows carry warnings — Ethiopia-shaped and the analogs have no held-out TOR skill once whole sites are held out. The corrected setup is the one that passes the disjoint-site TOR test cleanly, slope one-point-oh-one, and barely moves between protocols. Cohort engineering beyond this breaks the TOR test — this is the terminal IMPROVE-only candidate, which is why the remaining questions are for you rather than for more cohort work.

## Slide 7
At the CH band, ~91% of a raw Addis spectrum is background.
One real filter; the red dash is the baseline AIRSpec fits under it, per spectrum. The shaded sliver is the bands.
Python port validated against the group's R output to ≤ 6×10⁻⁷ absorbance. EDF 6 vs 8: indistinguishable.
baseline share @ CH ~91% (this filter)
port vs R ≤ 6×10⁻⁷
EDF 6 vs 8 Δslope < 0.01
ftir_31 §2.3 One real filter (median-like); grey = all 239 Addis spectra
Notes: SAY: Your baselining suggestion, implemented. Black line is one real filter — not an average; the red dash is the APRLssb segmented-spline baseline fitted under it, per spectrum. The shaded sliver is all that is actually bands. Two things for you specifically: the port is your algorithm — validated against your group's R output on the ETAD scans to six times ten-to-the-minus-seven absorbance. And your EDF question has an answer: six versus eight is indistinguishable, delta-slope under one hundredth.

## Slide 8
Addis rides a higher background than its calibration cohort.
Baseline height at 2920 cm⁻¹ per filter: cohort 0.101 vs Addis 0.170. Background structure does not transfer — and lands as an offset.
Baselining both sides: intercept −3.22 → −1.62, slope 1.59 → 0.86. Cost: R² 0.77 → 0.66, RMSE 1.16 → 2.41.
Addis vs cohort baseline 0.170 vs 0.101
intercept −3.22 → −1.62
ftir_31 §2.4 same filter, corrected
ftir_31 §2.5 baseline at 2920 cm⁻¹ per filter
Notes: SAY: Left: the same filter after subtracting its own baseline — the whole panel spans three hundredths of an absorbance unit against a raw spectrum of point-three-four. Right: baseline height at the CH band, one value per filter — the cohort medians point-one-oh-one, Addis point-one-seven-oh. Whatever a raw-spectra model learns about background does not transfer, and that error lands as an offset. Baselining both sides takes the intercept from minus three-point-two to minus one-point-six — the biggest single improvement of the project. Honest cost: Addis R-squared drops point-seven-seven to point-six-six and RMSE goes one-point-two to two-point-four. We prefer it for its residual structure, which is two slides ahead.

## Slide 9
The smoke calibration collapses on corrected spectra — its Addis response was mostly baseline.
Ann's objection: EC's sloping absorption lives partly in the baseline, so baselining should lose signal.
Evidence it was mostly not EC: smoke-906 falls 2.65 → 0.37 on corrected spectra, and the HIPS-transfer failure survives baselining — the break is compositional.
For Satoshi: how much real EC does the correction discard — and is a middle path worth testing?
smoke-906 corrected slope 0.37
HIPS transfer still fails
ftir_31 §1.2 All six setups, identical square axes, fixed 190-filter cohort, MAC = 10
Notes: SAY: All six setups on identical axes, fixed cohort, MAC ten. Ann's standing objection deserves saying out loud: EC's sloping absorption lives partly in the baseline, so baselining an EC calibration should LOSE signal. Our evidence that what we removed was mostly not EC: the 906-smoke model falls from slope two-point-six-five to point-three-seven when both sides are baselined — its raw response was largely memorised background — and the HIPS-transfer failure survives baselining, so what breaks at Addis is compositional. THE QUESTION FOR SATOSHI — probably the most important one today: how much genuine EC signal does full baseline removal discard? Is there a middle path — partial baseline retention — and where does your group's newer baselining work stand? Could we test it against AIRSpec on exactly this setup?

## Slide 10
The corrected model misses by a season-stable constant: −2.0 to −2.6 µg/m³.
Raw model: error tracks extrapolation distance (r = 0.71) and flips sign by season — out-of-domain failure.
Corrected model: flat, season-stable −2.0…−2.6. Bootstrap CI [−1.78, −1.06], excludes zero. Restated: ~21 Mm⁻¹ of absorption with no FTIR-EC behind it, MAC-invariant.
Deming with measured σ_x: −1.62 → −2.09 — OLS is the conservative bound (backup slide).
raw: resid ~ D² r = 0.71
corrected CI [−1.78, −1.06]
Deming λ* −1.62 → −2.09
ftir_31 §1.3 Residual vs Mahalanobis D²; site-cluster bootstrap B = 200
Notes: SAY: Residual against distance from the calibration cloud. The raw model's error tracks extrapolation — r point-seven-one — and flips sign by season: it fails by being out of domain. The corrected model's error is flat: distance-independent, season-stable, minus two to minus two-point-six. Bootstrap puts the corrected intercept at minus one-point-eight to minus one-point-one — excludes zero, disjoint from raw. A constant that survives every modelling choice looks like something additive in the x-axis data — restated as absorption, about twenty-one inverse megametres, forty-six percent of a typical Addis filter, and exactly MAC-invariant. IF THE ESTIMATOR comes up: with the measured HIPS uncertainty, Deming moves the corrected intercept to minus two-point-one — errors-in-variables makes the offset LARGER, so our OLS numbers are the conservative bound. Backup slides have the full four-estimator comparison.

## Slide 11
MAC cannot move any intercept — every calibration pivots; the fork is a slope contest.
x = Fabs/MAC: rescaling x by a constant keeps every intercept and R² exactly; slopes scale by exactly 0.6.
MAC 6 → raw models self-consistent (lowest-OC/EC 0.95). MAC 10 → the corrected model lands closest (0.86). Fit statistics cannot choose.
Estimator-independent: the pivot survives Deming exactly (backup slide).
slope scaling ×0.6 exact
raw @ MAC 6 0.95
corrected @ MAC 10 0.86
ftir_31 §1.4 Intercepts identical at both MACs; slope ×0.6 going 10 → 6
Notes: SAY: The algebra we promised. x is Fabs over MAC, so changing MAC rescales x by a constant — every setup keeps its intercept and R-squared exactly, and its slope scales by exactly point-six. So the intercept ladder is MAC-proof and the fork reduces to a slope contest: MAC six makes the raw models self-consistent — lowest-OC/EC point-nine-five — while MAC ten is where the corrected model lands closest at point-eight-six. Deliberately “lands closest”, not “self-consistent” — point-eight-six misses the slope-within-point-one bar the raw models clear. IF ASKED whether this depends on OLS: no — we redid it under Deming with the error ratio scaled correctly for the units change, and the pivot holds to machine precision. Backup slide.

## Slide 12
At Addis-like composition, IMPROVE's implied MAC is 10.05 — at the confirmed 633 nm.
Implied MAC = Fabs / TOR-EC across 151,843 matched IMPROVE filters. Pool median 11.96; the Addis-like OC/EC ≤ 2.27 subset (star, n = 6,503) sits at 10.05 — on the MAC = 10 line.
HIPS wavelength confirmed: He–Ne 632.8 ≈ 633 nm, MAC 10 defined at 633 (SPARTAN sources).
Addis-like subset MAC 10.05
pool median 11.96
high-OC/EC tail 19.8
ftir_31 §3 Rebuilt from the committed 151,843-filter table; headline numbers asserted in-notebook
Notes: SAY: The non-circular way to let data set MAC: where IMPROVE has both HIPS and TOR — a hundred fifty-two thousand filters — implied MAC is Fabs over TOR-EC. Pool median twelve; in the Addis-like OC/EC subset, the purple star, ten-point-oh-five. MAC ten is centred at Addis-like composition; MAC six is in the lower tail. And the high-OC/EC tail inflating to twenty shows Fabs carries organic-scaling non-EC absorption. One resolved fact worth stating: HIPS is confirmed as the helium-neon line, six-thirty-three nanometres, with MAC ten defined at six-thirty-three — SPARTAN's own Instruments page and the 2025 methods paper — so this bridge and the MAC convention are on the same wavelength. QUESTION FOR SATOSHI: does this chain hold up for you — and is there an independent HIPS MAC or protocol bridge that could test MAC-ten-at-Addis without new sampling?

## Slide 13
The 1600 band is not amine — and it is stuck below 1425 cm⁻¹ without your sub-1500 model.
Addis: 1617–1619 cm⁻¹ in every season. Every IMPROVE cohort: ≥ 1633. Co-varies with CH (ρ 0.88) and carbonyl (0.93), not with N–H/O–H (0.17) — amine rejected.
Carboxylate vs aromatic C=C needs the region below 1425 cm⁻¹: the sub-1500 model, or lab charcoal spectra (Emily Lee's, as data).
Addis center 1617–1619
IMPROVE cohorts ≥ 1633
ρ(1600, N–H) 0.17
ftir_31 §6 Group medians and IQRs from the committed ftir_12 stats table
Notes: SAY: Addis peaks at sixteen-seventeen to sixteen-nineteen in every season; every IMPROVE cohort sits at sixteen-thirty-three or higher, with essentially no overlap. Within Addis the band co-varies with CH and carbonyl but NOT with the N-H/O-H window — an N-H bend without its stretch is implausible, so amine is out. What remains — carboxylate versus aromatic C=C — cannot be separated on Teflon because the symmetric partner near fourteen-hundred is below the trusted range. TWO ASKS: where does the sub-1500 model stand — it is the unblocking tool here. And can we get Emily Lee's charcoal spectra as data — the paper versions are print-only, and the burning chemistry argument — O-H and aliphatic C-H destroyed, aromatic C=C grown, stronger with temperature — is the process case for the aromatic reading.

## Slide 14
Season changes loading, not shape — ftir_24 predicts dry and wet separately.
All bands, deployed EC (3.3 → 7.2 µg/m³) and Fabs (43 → 56 Mm⁻¹) peak in Kiremt; the 1600-band centre never moves; Dry has relatively more broad O–H.
Raw-model residuals by season: Dry −1.25 (worst) → Kiremt +0.49 (best); corrected is season-stable. ftir_24 quantifies with a season × x design.
EC by season 3.3 → 7.2
raw residuals Dry −1.25 → Kiremt +0.49
eval split 105 / 61 / 73
ftir_31 §5 Corrected spectra, median ± 10–90 % per season; joined via committed season labels
Notes: SAY: Naveed's seasons on the corrected spectra: everything peaks in Kiremt — deployed EC three-point-three to seven-point-two, Fabs forty-three to fifty-six — while the 1600-band centre never moves. The one shape effect is relatively more broad O-H in the Dry season. The committed residuals already show season sensitivity is a raw-model phenomenon: Dry is the WORST season for the raw model, minus one-point-two-five, Kiremt the best — inverted from what we'd guessed — while the corrected model is season-stable. ftir_24 is queued: per-season crossplots under the locked models with a pooled season-by-x design, because Dry spans only about half the wet x-range and naive per-season slopes attenuate mechanically.

## Slide 15
The one same-corridor TOR looks ordinary — and a second Ethiopian site sits unused.
Adama TOR: OC/EC 4.6–7.2 — the IMPROVE median, not the low tail. Reconciling Addis HIPS with FTIR OC at that composition needs MAC ≈ 47 m²/g — unphysical.
ETBI (Bishoftu): 26 HIPS filters, median 26.9 Mm⁻¹ — a free in-country test set, blocked only on the spectra pull.
Adama OC/EC 4.6–7.2
bridge MAC ≈ 47 m²/g
ETBI 26 filters, unused
ftir_31 §7 Rebuilt from the SPARTAN HIPS export + committed Adama TOR; medians asserted
Notes: SAY: The uncomfortable check: Adama's five quartz TOR filters give OC/EC four-point-six to seven-point-two — right at the IMPROVE median, not the extreme tail the Addis offset implies regionally. Reconciling Addis HIPS with FTIR OC at Adama-like composition would need a MAC around forty-seven — unphysical — so something has to give. And Bishoftu — ETBI, median Fabs twenty-seven against Addis's dry-season forty-three — is an untouched in-country test set for every conclusion today, IF its spectra come through. THE ASK: the INDH-CHTS spectra export, with ETBI added — same shape as the ETAD pull. It is the cheapest unblocking step on the whole list, and we have pre-registered the prediction: if the twenty-one megametres were a persistent background, ETBI's FTIR-EC should come out very low.

## Slide 16
What we need from you.
The headline: a co-located quartz-TOR campaign at ETAD or Bishoftu. Every EC reference we hold is circular with one axis or the other, and the surviving explanations for the ~21 Mm⁻¹ offset all yield to it. Spec: 11–13 days per season, ~36 filters total; Adama Batch-54 proves the chain. One-pager in hand.
Baselining trade-off
How much real EC does full baseline removal discard? Middle path / your newer method — worth testing vs AIRSpec?
Components
Is k = 4–5 defensible on corrected spectra? Must k match across models — run 5-for-all vs 20-for-all as a control?
Sub-1500 cm⁻¹ model
Status? It is the unblocking tool for carboxylate vs aromatic C=C at 1600.
Emily Lee's charcoal spectra
As data — the paper versions are print-only; replaces our failed KBr attempt.
INDH / CHTS / ETBI spectra export
Same shape as the ETAD pull; turns Bishoftu into a live in-country test set.
MAC / protocol bridge
Does the implied-MAC chain hold — any independent test of MAC ≈ 10 without new sampling?
Notes: SAY: Six things, one headline. Quartz TOR moved to the top this week because we closed every in-hand route to an independent EC reference — both ChemSpec carbon columns turned out circular, BC with Fabs and EC with our own FTIR-EC. The spec is written: eleven to thirteen days per season, about thirty-six filters TOTAL — not per season — and Adama Batch-54 proves the sampling-and-analysis chain works. Hand over the one-pager here. Then the five supporting asks, cheapest first: the spectra export unblocks the most for the least effort.

## Slide 17
BACKUP — Four regression estimators per setup: OLS is the conservative bound.
Same fixed cohort, four fits per setup: OLS, Deming at measured λ* = 2.96, constant-CV weighted Deming, Huber-robust Deming.
Every errors-in-variables treatment deepens the intercept — OLS is the conservative bound. The corrected setup moves least (−1.62 → −2.09).
λ* 2.96 (measured)
corrected, Deming 0.95x − 2.09
ftir_31 §1.10 OLS rows asserted against the committed setup matrix
Notes: SAY (if the estimator question comes up): every crossplot today used OLS, which assumes all error in y. Refit with errors in both axes — Deming at the measured error ratio, a constant-CV weighted variant, and a Huber-robust variant — every setup's slope steepens and its intercept goes MORE negative. So the numbers on the slides are the conservative bound on the offset. The corrected setup moves least: minus one-point-six-two to minus two-point-one across all four. The OLS rows here are asserted against the committed matrix in the notebook.

## Slide 18
BACKUP — The MAC pivot survives Deming exactly.
Filled/solid = MAC 10, open/dashed = MAC 6, diamond = the shared intercept. All fits Deming, λ scaled with MAC².
Asserted per setup: intercept identical at both MACs (to 10⁻⁹); slope ×0.6 exactly. The MAC-proof result is estimator-independent.
λ @ MAC 10 / 6 2.96 / 1.07
pivot exact under Deming
ftir_31 §1.11 Every fit Deming; OLS intercepts quoted per panel for reference
Notes: SAY (if asked whether MAC-proof depends on OLS): no. Redone under Deming with the error-variance ratio scaled with MAC squared — the correct error model when you rescale x — the intercept is identical at both MACs to ten-to-the-minus-nine and the slope scales by exactly point-six, per setup, asserted in the notebook. Deming deepens every intercept relative to OLS, but the structure is untouched: MAC still cannot move any intercept.